## Slide 1: A lesson of Physical Computing with Scratch: RPi, scratchClient and Arduino
Presentation for Pi And More 9½
Krefeld – 2017/01/14
Hans de Jong

## Slide 2: Weekendschool
Generally parents tell their children: “Learn for later”. But what is later?
“I want to become an engineer. Do you maybe know an engineer? I would very much like to meet one”
EINDHOVEN Xxx students
Trudo Weekendschool
IMC Weekendschool

## Slide 3: Weekendschool
Goal and way of working
Bridge the gap between school and what is needed to live in society
  Which is in more privileged families provided by the family
Don’t abandon them at the end: Alumni program
Data shows: alumni have better professional prospects, are more self-aware, and feel more connected with society.
Program includes training in presentation, research, debate, and conflict resolution – an allround character education.
Some numbers
> 1000 students in 2016 between 10 and 14 years of age
From disadvantaged neighborhoods
3500+ volunteers
Funded by 110+ sponsors (companies, individuals, foundations)
Curriculum lasts for 2.5 to 3 years
Over 2100 alumni
Students are selected on motivation, not on IQ
IMC Weekendschool founded in 1998, Trudo Weekendschool in xxx
IMC Weekendschool has inspired 30+ other independent copy projects in The Netherlands (one of which is the Trudo Weekendschool).
Classes provided
Art
Medicine
Law
Philosophy
Astronomy
Politics
Mathematics
Physics
Programming
Film
Architecture
Entrepreneur
Language & Poetry
Safety
Energy
Journalism
… many more
More information
www.imcweekendschool.nl
www.trudoweekendschool.nl

## Slide 4: Curriculum of Programming
Objectives
Learn how to use keyboard, mouse and screen without causing health problems.
Learn how to make programs in Scratch
Learn that programming is about more than changing pixels on a screen (Physical Programming).
Learn something about professional programming.
Build something tangible that can be taken home.
Let the children experience how powerful and joyful programming is.
3 lessons
Each is 2x 75 minutes with 30 minutes break inbetween
Given to Weekendschool 2nd graders: 11 years old.

## Slide 5: The 3 lessons of the curriculum
Lesson 1
Program a game in Scratch, output on monitor.
1 helper per 8 students.
Lesson 3
program an Arduino Nano from Rpi. Complete the electronic circuit of a game to be able to take home. 1 helper per 2 students.
  Could also be done in 2 lessons.
Lesson 2
physical computing controlled from Scratch. 1 helper per 4 students.
  Could also be done in 2 lessons.

## Slide 6: The hardware of lesson 2

## Slide 7: The setup
Arduino Nano
Raspberry Pi
2B or 3B
Scratch 1.4 run time
scratchClient
scratchClient Sketch
scratchClient Config file
Program in Scratch
Powered USB hub
(not strictly needed since Arduino is powered separately – used for protection of Rpi)
Remote Sensor Protocol Over socket 42001
Global variables
Broadcasts
Defines function of the GPIO pins on the Arduino (and RPi) and gives them logical names.
Predefined sprites (with some code, sounds and costumes)
Standard setup
Programmed by the students
Prepared by the teacher

## Slide 8: The game
Start the game by pressing the joy stick button (because it is there anyway)
Red LED lites at random
When LED lites, the first one pressing their button gets a point
  The duck turns to the person scoring and makes a bow.
When the button is pressed without the LED being lit, the other gets a point
  The duck turns to the one who pressed and shakes “no”.

## Slide 9: Demo of the game

## Slide 10: Why using an Arduino for GPIO rather than the GPIO of Raspberry Pi?
Arduino provides analog inputs.
Arduino provides hardware PWM (Pulse Width Modulation), which makes controlling servos more stable.
Arduino can support real time protocols (e.g. for controlling WS2812).
Arduino GPIO pins are 5V tolerant.
When making mistakes, blowing up an Arduino Nano is less costly (< 2.5 euro for a clone) than damaging a RPi.
When needing more GPIO pins, extra Arduinos can be added.
  scratchClient supports this as beta.
Easier setup and tear down in temporary classroom situations
  Only needing to plug/unplug USB and power connectors.
  Can be programmed to steer servos automatically to default position, ready for packing up.

## Slide 11: scratchClient: things to know
Installing
Download scratchClient
  http://heppg.de/ikg/wordpress/?page_id=6
Unpack
Install other packages as described in the documentation
Adapt the config file for Arduino and put it in a place of your own.
Use the Arduino IDE to program the scratchClient sketch in the Arduino
  Note: when using Arduino clones, programming via Raspberry Pi only works till Raspian release xxxx. Don’t understand why it fails in later releases.
Start scratchClient with the correct config file as parameter.
Good to know about the scratchClient config file
Input / output …

## Slide 12: Cost and effort for the board
See Bill of Material on the next slide.
Material cost for a single piece: ca. 20 euro, but you will have extra material.
Material cost for a series for e.g. a school: can get sub 20 euro.
Labour content (no compensation included): ca. 2.5 hour.
Most components were ordered from Aliexpress.com.
  Benefits
    Extremely low prices.
    Almost always shipped for free to The Netherlands, Germany and probably other EU countries.
      Counterintuitive: the smaller the order, the more chance that there are no shipment costs.
  Disadvantage
    Delivery takes between 2 weeks and 2 months
      Or arrives never (some 2% of shipments), but then refund is promptly done
    Especially for power supplies: do not expect more than 50% of current that is rated.
      Otherwise it will overheat and blow up. Or the voltage drops way below what is needed.
    Occasionally products are quickly running out
      So make sure you order quickly the amount you need and some spare for the future.
Note: limit each order to max 22 euro (holds for all of the EU) if you want to avoid VAT, import duties and handling costs at the shipping company.
Secure payment possible (at least in The Netherlands: you can use IDEAL).

## Slide 13: BOM (Bill of Material)

## Slide 14: What can scratchClient do further?
Control all the GPIO pins on Raspberry Pi.
Run on PC and in combination with Arduino provide physical computing to Scratch on running on Windows.
Watch all the variables in the RPis from a central PC.
Allow to use Arduino Uno instead of Arduino Nano
Keep apart multiple connected Arduino Nanos and address the right GPIO pins on the correct Nano
  So the number of connectable peripherals is virtually infinite.
My conclusion:
scratchClient is the ideal software to bring physical computing to Scratch.

## Slide 15: More information
This presentation and source files of the game
  www.github.com and search for Weekendschool
scratchClient
  http://heppg.de/ikg/wordpress/?page_id=6
Scratch
  https://scratch.mit.edu/
Raspberry Pi
  https://www.raspberrypi.org/
Arduino
  https://www.arduino.cc/

## Slide 16: Try for yourself?
Attend my workshop at 13.00 today
  Registration mandatory (with the Pi And More organisers)
  Hurry up, because the amount of places is limited

## Slide 17: Making a workplace for 2 students
Raspberry Pi 3B
  With power supply
  With 16 GB microSD card
Second hand monitor HP1750 or HP1740
Second hand keyboard
Second hand mice (2x)
  so they can each use a mouse and can be instructed: learn to use your left hand for the mouse as well.
MDF 9mm board (better: 2x 4mm with 12 mm filler in between)
  See further the pictures
For 2 workplaces opposite of each other: 2 laths, 4 clamps, 4 threaded rods M8, 4 nuts, 8 large washers, 12 butterfly nuts.
84 liter crates of RUB (Really Useful Boxes, http://www.reallyusefulproducts.co.uk/) can very precisely contain 4 monitors (2 dismounted from their pedestal) and cables.
Ergonomics: keyboard at the correct height to teach children to pay attention to how they sit when using computers to avoid medical problems (RSI) later in life.

## Slide 18: Questions?