## Slide 1: Physical computing: control servos, LEDs and more from Scratch using RPi, Arduino, scratchClient
Hans de Jong
Pi And More 9½
Krefeld – 14 January 2017

## Slide 2: Workshop organisation
10 mins Welcome and introduction presentation.
After that everyone will work at his or her own pace.
At times I will present for 5 minutes to explain a next concept.
Language: English, but help in German available.
If you want to also work with the game used at the Weekendschool, say so 30 minutes before the end of the workshop.
  Then you can get something working
At the end:
  Copy the material you worked on to a USB stick (if you brought one)
  Copy a complete image (compressed, < 1 GB) to a USB stick
  Pull all components and wires from the breadboard and put in the plastic box that is now on your table.

## Slide 3: Objectives
At the end of today you should be able to:
  Reproduce the setup at home (provided you have the hardware  )
  Understand
    Digital output (e.g. liting a LED)
    Digital input (e.g. sensing a button)
    Analog input (e.g. from a potentiometer)
    Pulse Width Modulation (PWM)
      for dimming LEDs
      For controlling servos
      For controlling a buzzer
  Understand what all these resistors are for
  Be able to configure scratchClient
If time permits / as you desire: look at a game using servos, buttons, LEDs etc as used on the Weekendschools in The Netherlands.
Have fun!

## Slide 4: Only a few rules
If Raspberry Pi needs to be rebooted, it needs a powercycle. Please do not pull plugs but use the switch in the outlet.
Always put a resistor in series with the components
  If you think there is no need then please tell us and we will explain why this IS required.
When changing the wiring
  Stop scratchClient
  Detach the USB cable and switch off the 9V power
  Check, double check and check again whether the wiring is correct.
    You may blow up components
  Make sure that you both are convinced the wiring is OK before turning on power again.
If something breaks down or gets damaged: we have some spare material
  Do not put anything that is broken back into the box.

## Slide 5: Lessons at the Weekendschool

## Slide 6: What do you have at your desk?

## Slide 7: Where is the presentation?
You will find this presentation = the instruction at your desktop in PiAndMore/Part-1--Breadboard
If you already know the stuff and get bored then feel free to work on your own
  Silently please

## Slide 8: Breadboard

## Slide 9: Looking at the Arduino extension board

## Slide 10: Looking at the scratchClient config file

## Slide 11: Uploading scratchClient to the Arduino

## Slide 12: The first thing – as always
Get the “Hello World” experience
  Get something working so that you see it is worth continuing

## Slide 13: Digital Output

## Slide 14: Digital Input

## Slide 15: Analog input

## Slide 16: Pulse Width Modulation (PWM)

## Slide 17: Controlling a servo with PWM

## Slide 18: Dimming a LED with PWM

## Slide 19: Expanding

## Slide 20: Tri-color LED with PWM

## Slide 21: Control a passive buzzer with PWM

## Slide 22: Add a Joystick