## Slide 1: Physical computing: control servos, LEDs and more from Scratch using RPi, Arduino, scratchClient
Hans de Jong
Pi And More 9½
Krefeld – 14 January 2017

## Slide 2: Ergonomics
At the Weekendschool we teach children 5 golden rules how to sit when using computers:
  Rest your arms on the table in a natural fashion.
  If you do not need the keyboard, move it up and give room to the mouse.
  Have the monitor at arms length.
  Change position (lean forward, backward etc.).
  Frequently stop, walk around and excersize.
To change the height, use the two upper wingnuts.

## Slide 3: Workshop organisation
Welcome and introduction presentation (10 min).
After that everyone will work at his or her own pace.
At times we will present for 5 minutes to explain a next concept.
Language: English, but help in German available.
At the end copy to your USB stick (if you want) and cleanup.
The major steps:
  Get a working hardware and scratchClient config using a Scratch test program.
  Update scratchClient config (moving to other GPIO pins)
  Write your own Scratch program to access the board.
  Add more hardware (buzzer, tri-color LED, button, joy stick) and adapt scratchClient config and adapt the Scratch program.
  If you want: have a look at the game used at the Weekendschool and program a bit yourself (but it is still in Dutch  )
    Start latest 30 minutes before the end of the workshop.

## Slide 4: Objectives
At the end of today you should be able to:
  Reproduce the setup at home (provided you have the hardware  )
  Understand
    Digital output (e.g. lighting a LED)
    Digital input (e.g. sensing a button)
    Analog input (e.g. from a potentiometer)
    Pulse Width Modulation (PWM)
      for dimming LEDs
      For controlling servos
  Understand what all the resistors are for
  Be able to configure and run scratchClient
  Program Scratch to control the physical input and output
If time permits / as you desire: look at a game using servos, buttons, LEDs etc. as used on the Weekendschools in The Netherlands.
Have fun!

## Slide 5: Non-objective
It is not an objective to create a complete useful game or other program.
  You can do that with your own creativity at home now that you know how to control several pieces of hardware from Scratch using scratchClient.

## Slide 6: Weekendschool
Generally parents tell their children: “Learn for later”. But what is later?
“I want to become an engineer. Do you maybe know an engineer? I would very much like to meet one”
Professionals teach children on Sundays about their job. Large variety of topics.
> 1000 students between 11 and 14 years from underprivileged areas.
Curriculum lasts for 2.5 to 3 years
3500+ volunteers.
Funded by 110+ sponsors (companies, individuals, foundations).
Started in 1998.
It works! Data shows: alumni have better professional prospects, are more self-aware, and feel more connected with society.
EINDHOVEN 58 students
Trudo Weekendschool
IMC Weekendschool

## Slide 7: Lessons at the Weekendschool
I personally teach
  Mathematics (since 12 years)
  Physics (since some 6 years)
  Programming (started this 2016)
  Electro (started this 2016)
Programming: 3 lessons on 3 Sundays with Scratch, Raspberry Pi and Arduino
Lesson 2: Physical computing: https://youtu.be/Qo1gnXNzhqE

## Slide 8: Only a few rules
If Raspberry Pi needs to be rebooted, it needs a powercycle. Please do not pull plugs but use the switch in the outlet.
Always put a resistor in series with the components
  If you think there is no need then please tell us and we will explain what the reason is (with one exception).
When changing the wiring
  Stop scratchClient (just close the window)
  Detach the USB cable from the Arduino Nano
  Switch off the 9V power
  Check, double check and check again whether the wiring is correct. You may blow up components when wiring wrongly.
  Make sure that you both (4 eyes principle) are convinced the wiring is OK before turning on power again.
If something breaks down or gets damaged: we have some spare material
  Do not put anything that is broken back into the box please.

## Slide 9: The setup
Arduino Nano
Raspberry Pi
2B or 3B
Scratch 1.4 run time
scratchClient
scratchClient Sketch
scratchClient Config file
Program in Scratch
Powered USB hub
(not strictly needed since Arduino is powered separately – used for protection of RPi)
Remote Sensor Protocol Over socket 42001
Global variables
Broadcasts
Defines function of the GPIO pins on the Arduino (and RPi) and gives them logical names.
Predefined sprites (with some code, sounds and costumes)
Standard setup
Programmed by the students
Prepared by the teacher

## Slide 10: Where is the presentation?
You will find this presentation = the instruction at your desktop in PiAndMore/Part-1--Breadboard
If you already know the stuff and get bored then feel free to work on your own
  Silently please … 

## Slide 11: Breadboard
Used to quickly build electronic circuits
Note the 2 rails for + (VCC) and – (GND)
Note the 2 bars with 5 interconnected holes each.

## Slide 12: Looking at the Arduino Nano extension board
9V power socket
Arduino Nano with 328P processor
Micro USB port
Per GPIO signal 3 headers:
S (blue = signal)
V (red = VCC = +)
G (black = GND = -)
(very handy to e.g.
connect servos)
Digital ports
Analog ports
Reset button
Reset button

## Slide 13: Uploading scratchClient to the Arduino
Make sure that the Arduino is directly connected to the Raspberry Pi (not via the USB hub)
Open the scratchClient sketch for Arduino Uno
Double click to open the Arduino IDE
Click tools and make sure that these are set:
  Board: Aruino Nano
  Processor Atmega328
  Port: the port where the Arduino Nano is connected
Click on the Upload button.
Wait till the completion of the Upload is reported.

## Slide 14: Open the scratchClient config file
Note: it is called config_arduino_uno.xml, however it also is for the Nano.

## Slide 15: Looking at the scratchClient config file
Note that every definition on the left has a line on the right. Note that the directions are counter intuitive.

## Slide 16: Let’s wire the board …
See diagram on the next page
Wire +5V to the + rail at the bottom
Wire GND to the – rail at the bottom
Wire a red LED to pin 4.
  Pin 4  200 Ohm resistor  GND (minus)
Wire another LED (we use blue) to pin 7.
  Pin 7  200 Ohm resistor  - (minus) rail
Wire a button to pin 3.
  Pin 3  1 kOhm resistor  GND (minus)

## Slide 17: First step: red LED and + and -

## Slide 18: Second step: add button and blue LED
This is the very thin resistor

## Slide 19: Why are these resistors needed?
In series with a LED: to limit the current through the LED
  You may blow up the LED and/or the Arduino otherwise.
In series with buttons, potentiometers etc: to avoid blowing up the Arduino in case of config errors
Arduino
+5 Volt
0 Volt
30 kOhm
1 kOhm
Digital input
Consider what would happen if the 1 kOhm resistor were not there and the port would be used as output and the button closed.
Then the Arduino would output 5 Volt, and the switch is directly leading it to the 0 Volt line  short circuit!

## Slide 20: Check / double check
Please now check both that the wiring is correct.

## Slide 21: Make a script file to start scratchClient
Copy the config file to the desktop.
  We will later modify it and want to keep the original.
Then make a new file on the desktop
  Call it StartSC_First step
Put this in:
  sudo python ~/scratchClient/src/scratchClient.py -c ~/Desktop/config_PiAndMore_ttyUSB0.xml
Make the file executable.
Do you understand what the file does?
  If not, please ask

## Slide 22: Bringing things together
Connect the 9 Volt connector to the board
Connect the USB connector to the Arduino
Start scratchClient with the script you just made
Start the Arduino Scratch test. This is in:
Press the green flag to start the Scratch program.

## Slide 23: Does it work?

## Slide 24: Analog input
Note: only the additional wires are shown.

## Slide 25: Pulse Width Modulation (PWM)

## Slide 26: Controlling a servo with PWM
The position of the servo is changed by sending pulses of different width.
The servo looks at the pulsewidth and turns as desired.

## Slide 27: Dimming a LED with PWM
Put the green LED in the right place.

## Slide 28: Add a Joystick
The joy stick consists of
  Potentiometer for X
  Potentiometer for Y
  Button
Wire these 3 signals via a 1 kOhm resistor on the breadboard to pins A1 and A2 for X and Y and the button to one of the digital porst
Adapt the scratchClient config
Once it runs, you can see values for the potmeter as sensors in Scratch.

## Slide 29: More information
This presentation, source files of the game and workshop material
  www.github.com and search for Weekendschool or for PiAndMore
scratchClient
  http://heppg.de/ikg/wordpress/?page_id=6
Scratch
  https://scratch.mit.edu/
Scratch on Raspberry Pi
  https://www.raspberrypi.org/forums/viewforum.php?f=77
Raspberry Pi
  https://www.raspberrypi.org/
Arduino
  https://www.arduino.cc/